## Slide 1: Embedded Networking Software Development Lab 2 – Networking Layer 3 (Network Layer)
Version 0.1

## Slide 2: Overview
Purpose
  Learn how the “ping” command is implemented in an IPv4-based networking stack.
Learning objectives
  To become familiar with the packet formats of the IPv4 and ICMP protocols
  To learn how the “ping” command is implemented in an embedded networking stack for the FRDM-K64F board.

## Slide 3: Overview (2)
The FRDM-K64F board
Ethernet RJ-45 port
Micrcontroller
(Kinetis K64F)
Ethernet PHY
(Micrel KSZ8081RNA)

## Slide 4: Background Information
The IPv4 protocol (Internet Protocol version 4)
  Layer 3 protocol in the OSI model

## Slide 5: Background Information
The IPv4 protocol (2)
  Carries layer 4 packets
    UDP datagrams
    TCP segments
  Carries layer 3 control packets
    ICMP messages
    IGMP messages
  Carried in a layer 2 protocol such as Ethernet
    An IPv4 packet is encapsulated in an Ethernet frame, using the value 0x0800 for the frame type field

## Slide 6: Background Information (2)
The ICMP protocol
  Internet Control Message Protocol
  ICMPv4 messages are encapsulated in IPv4 packets
    Protocol field of the IPv4 header is set to the value 0x01

## Slide 7: Background Information (3)
The “ping” command
  Ping uses ICMP messages
  It sends an ICMP “echo request” message to the target host and waits for an ICMP “echo reply” message from the target host.
Ping request ICMP message
  Type = 8, Code = 0
Ping reply ICMP message
  Type = 0, Code = 0

## Slide 8: Lab Overview
Networking Stack Architecture
Lab2: IPv4

## Slide 9: Lab Overview (2)
Instructions:
    Complete the code that implements the minimum support for the ICMP protocol in the embedded networking stack for the FRDM-K64F board, to be able to send and reply to “pings”:
      Solve the 7 TODOs in the networking_layer3_ipv4.c source file.

## Slide 10: Test Plan
  Test your completed embedded networking stack on the FRDM-K64F board, by using the following test cases:
    Test case 1: “ping” from the FRDM-K64F board to the PC
    Test case 2: “ping” from the PC to the FRDM-K64F board
    Run test cases from lab1 to verify that there are no regressions
  Test Environment Configuration:
    Connect the Ethernet port of the board to the Ethernet port of your PC
    Configure a static IPv4 address for the PC’s wired Ethernet interface that is in the 192.168.8.0/24 subnet (e.g., 192.168.8.1)

## Slide 11: Test Plan (2)
  Test Case 1: Ping from the FRDM-K64F board to the PC
    Run the “ping” command from the FRDM-K64F board to the PC, from the TeraTerm window:

## Slide 12: Test Plan (3)
  Test Case 2: Ping from the PC to the FRDM-K64F board
    Run the “ping” command from the PC to the FRDM-K64F board, from a Command prompt window or a PowerShell window:

## Slide 13: Test Plan (4)
  Test Case 3: Command messages
    Send “command” messages to the board to change the color of the blinking LED. Valid commands are the strings: “red”, “green”, “blue”, “yellow”, “cyan”, “magenta” and “white”.

## Slide 14: Test Plan (5)
  Test Case 4: Wireshark Analysis
    Use Wireshark to examine the “ping” ICMP packets:

## Slide 15: Test Plan (6)
  Test Case 5: Board Network Stats Analysis
    Start a TeraTerm session and connect it to the board’s serial console
    While doing pings from the board to the PC and from the PC to the board, look at the Network stats dashboard on the board’s serial console. Verify the consistency of the stats (e.g., # of packets received at layer 3 cannot be greater than # of packets received at layer 2)

## Slide 16: Software Architecture Diagrams
Hardware/Software Topology

## Slide 17: Software Architecture Diagrams (2)
Hardware Context Diagram

## Slide 18: Software Architecture Diagrams (3)
Software Context Diagram

## Slide 19: Software Architecture Diagrams (4)
Runtime Architecture

## Slide 20: Software Architecture Diagrams (5)
Runtime Architecture (cont.)