## Slide 1: Embedded Networking Software Development Lab 3 – Networking Layer 2 (Link Layer) and Layer 1 (Physical layer)
Version 0.1

## Slide 2: Overview
Purpose
  Learn how the ARP protocol works and to get exposed to Ethernet as a layer-2 networking technology.
Learning objectives
  To become familiar with the packet format of the ARP protocol
  To become familiar with the Ethernet frame format
  To learn how to detect if there is physical Ethernet connectivity (physical Ethernet link is up or down)

## Slide 3: Overview (2)
The FRDM-K64F board
Ethernet RJ-45 port
Micrcontroller
(Kinetis K64F)
Ethernet PHY
(Micrel KSZ8081RNA)

## Slide 4: Overview (3)
  In lab2, we used Wireshark to examine the “ping” ICMP packets (shown in pink below):
When a network interface is “turned on”, a gratuitous ARP request is sent for its local IPv4 address, to detect if someone else is using the same IPv4 address
When sending a packet for the first time to a new node, an ARP request is sent to all nodes in the same subnet, to see who has the target IP address
The target node replies with an “ARP reply” message to the requesting node. The ARP reply contains the local MAC address of the node sending the reply.

## Slide 5: Background Information
To be transmitted over the network, IPv4 (and IPv6) packets are encapsulated in layer-2 packets.
  In the case of Ethernet, layer-2 packets are known as Ethernet frames
Also, layer-3 node addresses need to be mapped to layer-2 node addresses.
  In the case of Ethernet, layer-2 addresses are known as MAC (Media Access Control) addresses, and nodes as known as Ethernet stations.
  The Address Resolution Protocol (ARP) maps IPv4 addresses to layer-2 addresses.
    It is a layer 2.5 protocol, as it has “one foot on layer 3 and one foot on layer 2”.

## Slide 6: Background Information (2)
The ARP Protocol has two basic message types:
  ARP Request
    Carried in a layer-2 broadcast packet
    Its purpose is to ask other nodes in the same layer-2 network (layer-3 subnet) “who has a given IPv4” address.
    There is a special ARP request known as a “Gratuitous ARP request”, used to detect duplicated IPv4 addresses in a subnet.
  ARP Reply
    Carried in a layer-2 unicast packet
    Its purpose is to answer an ARP request to the requesting node, by providing the layer-2 address of the node that has the given IPv4 address (contained in the ARP request)

## Slide 7: Background Information (3)
The ARP Protocol basic flow:
  When an IPv4 node’s network interface is “turned on”, or its IP address is changed, the networking stack sends a gratuitous ARP request, to make sure that no other nodes (in the same subnet) have the same IP address.
    No ARP reply should be received, unless there are two or more nodes with the same IPv4 address, which is a network configuration error.
  When an IPv4 node sends an IPv4 packet to another node, for which its layer-2 address is not known, the networking stack sends an ARP request, to obtain the target node’s layer-2 address, before it can send the IPv4 packet.
  When an IPv4 node receives an ARP request for its own IPv4 address, the networking stack sends an ARP reply to the requesting node.

## Slide 8: Background Information (4)
The ARP Protocol basic flow (cont.):
  When the node that sent the ARP request receives an ARP reply for the target IPv4 address, it saves it in a table known as the ARP cache, and sends the pending IPv4 packet(s).
    Subsequent sends of IPv4 packets will get the target node’s layer-2 address from the ARP cache instead of sending ARP requests.
    Entries in the ARP cache expire after 20 minutes, by default. After that, the next packet send will trigger a new ARP request.

## Slide 9: Background Information (5)
Fields of an ARP message:
  Link address type
    0x1 for Ethernet MAC addresses
  Network address type
    0x800 for IPv4 addresses
  Link address size (in bytes)
    6 for Ethernet MAC addresses
  Network address size (in bytes)
    4 for IPv4 addresses
  ARP operation (ARP_REQUEST or ARP_REPLY)
    16-bit value in network byte order
    0x0001 – ARP request
    0x0002 – ARP reply

## Slide 10: Background Information (6)
Fields of an ARP message (cont.):
  Source (sender) link address
    Sender’s MAC address in the case of Ethernet
  Source (sender) network address
    Sender’s IPv4 address
  Destination (target) link address
    Target’s MAC address in the case of Ethernet
  Destination (target) network address
    Target’s IPv4 address

## Slide 11: Background Information (7)
Ethernet MAC addresses
There are two special MAC addresses:
Broadcast MAC address:
ff:ff:ff:ff:ff:ff
Null MACV address:
00:00:00:00:00:00

## Slide 12: Background Information (8)
Ethernet Frames
  Both IPv4 packets and ARP messages are carried in Ethernet frames
Fields of an Ethernet frame
  Destination MAC address
  Source MAC address
  Frame type
    0x0800 – for IPv4 packets
    0x0806 – for ARP messages
    0x8100 – for VLAM tagged frame
    0x86dd – for IPv6 packets
  Data payload (e.g., IPv4 packet, ARP message, etc)
  CRC

## Slide 13: Background Information (9)
Ethernet MAC
    Media Access Controller
    Implements a data-link layer (layer 2 of the OSI model).
    A hardware module inside a microcontroller chip such as the NXP Kinetis K64F
Ethernet PHY
    Physical interface transceiver
    Implements the physical layer (layer 1 of the OSI model)
    A separate chip such as the Micrel KSZ8081RNA

## Slide 14: Background Information (10)
MII
    Media Independent Interface
    Hardware protocol for chip-to-chip communication between the Ethernet MAC (in the microcontroller) and the Ethernet PHY
    Consists of a parallel data interface and a serial management interface
    Data interface is full duplex (separate signals for Rx and Tx) and requires 16 pins in total
    Requires a 25MHz clock
    Supports data transfer rates up to 100 Mbits/s
    Serial Management Interface (SMI) also known as MDIO, requires two pins.
      Multiple PHYs can be connected to the same MDIO bus.
      Each PHY on a MDIO bus has its own address

## Slide 15: Background Information (11)
RMII
    Reduced pin-count MII
    Data interface requires only 8 pins
    Requires a 50MHz clock
SMII
    Serial MII
    Data interface requires only 4 pins
    Requires a 125MHz clock

## Slide 16: Background Information (12)
Higher speed MAC-to-PHY protocols
    GMII - Gigabit MII: 1 Gbits/s
    RGMII - Reduced pin-count GMII
    SGMII - Serial GMII
    QSGMII- Quad Serial GMII (4 SGMII lines combined): 5 Gbits/s
    XGMII - 10 Gigabit MII: 10 Gbits/s

## Slide 17: Background Information (13)
Pin connections between the MCU (K64F chip) and the Micrel Ethernet PHY (KSZ8081RNA chip)
MDIO serial bus signals
- PTB1 means: K64F GPIO Port B, Pin 1
RMII signals

## Slide 18: Lab Overview
Networking Stack Architecture
Lab3:
Lab3:
Lab3

## Slide 19: Lab Overview (2)
Instructions:
    Implement the TODOs tagged with ‘TODO-lab3’ in the code of project lab3-layers2and1:
      Complete function that send an ARP request
      Complete function that sends an ARP reply
      Complete function that sends an Ethernet frame
      Configure the MDIO pins of the Ethernet PHY
      Implement function to detect if the Ethernet physical link is up/down
      Complete function that generates local MAC address for the FRDM-K64F’s Ethernet interface.
    Answer question in the QUESTIONS.txt file

## Slide 20: Test Plan
  Test your completed embedded networking stack on the FRDM-K64F board, by using the following test cases:
    Test case 1: “ping” from the FRDM-K64F board to the PC
    Test case 2: “ping” from the PC to the FRDM-K64F board
    Run test cases from lab1 to verify that there are no regressions
  Test Environment Configuration:
    Connect the Ethernet port of the board to the Ethernet port of your PC
    Configure a static IPv4 address for the PC’s wired Ethernet interface that is in the 192.168.8.0/24 subnet (e.g., 192.168.8.1)

## Slide 21: Test Plan (2)
  Test Case 1: Ping from the FRDM-K64F board to the PC
    Run the “ping” command from the FRDM-K64F board to the PC, from the TeraTerm window:

## Slide 22: Test Plan (3)
  Test Case 2: Ping from the PC to the FRDM-K64F board
    Run the “ping” command from the PC to the FRDM-K64F board, from a Command prompt window or a PowerShell window:

## Slide 23: Test Plan (4)
  Test Case 3: Command messages
    Send “command” messages to the board to change the color of the blinking LED. Valid commands are the strings: “red”, “green”, “blue”, “yellow”, “cyan”, “magenta” and “white”.

## Slide 24: Test Plan (5)
  Test Case 4: Detection of Ethernet link up/down
    Unplug the Ethernet cable that connects the FRDM-K64F board to the PC, from either end.
      The board’s RGB LED should blink red
    Re-plug the unplugged end of the Ethernet cable that connects the FRDM-K64F board to the PC
      The board’s RGB LED should blink green

## Slide 25: Software Architecture Diagrams
Hardware/Software Topology

## Slide 26: Software Architecture Diagrams (2)
Hardware Context Diagram

## Slide 27: Software Architecture Diagrams (3)
Software Context Diagram

## Slide 28: Software Architecture Diagrams (4)
Runtime Architecture

## Slide 29: Software Architecture Diagrams (5)
Runtime Architecture (cont.)